Control Systems

W. Lopez, CSULB – ET 360

Activity 10 Motor Speed Monitor with LabView Virtual Instruments

1)  Objective of Lab:

  - The following concepts will be introduced and applied with the goal of becoming familiar with the LabVIEW application and its interface:

    - New Dialog Box and Template VIs

    - Front Panel

    - Block Diagram

    - Front Panel and Block Diagram Tools

    - Running and Stopping a VI

    - Express VIs

    - LabVIEW Documentation resources

    - Property Dialog Boxes

    - Shortcuts

- Procedure:

Motor and DAQ Connections

- Attach DAQ to computer through USB cable

  - Motor leads:

    - Blue – (-)

    - Red – (+)

- Tachometer:

    - Yellow – (+) Pin 5 on the DAQ A/1

    - Green – (-)   Pin 6 on the DAQ A/1

    - Connect these to the DAQ channels 5 and 6 (AI1 (+) & (-))

Block Diagram Panel

- On the Block diagram page place a DAQ Assistant

  - Right Click

  - Express

  - DAQ Assistant

  - Click and drag DAQ Assistant into the Block Diagram page

  - NI-DAQ Assistant Screen appears

    - On right side click Acquire Signals

    - Select Analog Input

    - Select Voltage

    - Select AI1 and click finish

  - Signal Input Range

    - Select Max: 20 & Min -20

    - Change (at bottom) rate (Hz) – 10k

**	Turn Page

  - Click Run at top

    - A sine wave should appear

    - If not apply voltage motor (4 VDC)

    - If so click ok at bottom DAQ Assistant window

    - DAQ Assistant window should exit and Block diagram should reappear

- Place a while loop on the Block Diagram

  - Express

    - Exec Control

      - While Loop – make sure all components are inside

- Place Timing & Transition Measurements

  - Express

    - Signal Analysis

      - Timing - Trans… - place on block diagram to the right of the DAQ

        - Select Frequency

- Place Formula – to the right of Timing and Transition Meas.

  - Express

    - Arith & Compar

      - Formula – place to the right of the Timing & Trans Meas.

        - Under Label – replace X1 with f

        - In the open space above type:

          - (click X1 [under Input and f should appear] * 60) / 8

          - This should look like this: (f*60)/8

          - This is motor speed equation (Spd = (freq x 60) / pairs of poles

          - Click ok

Front Panel

- Place Waveform Graph

  - Modern

  - Graph

    - Waveform Gr… - place next to STOP button

- Place Numeric Indicator

  - Numeric Indic… - place above Waveform Graph

  - Repeat for second indicator

Block Diagram Panel (2)

- Organize waveform graph, numeric indicator 1 and 2

- Make room inside while loop as necessary

- DAQ Assistant must connect to Timing & Transition Measurements

  - DAQ Assistant Data must connect to Timing & Transition Measurements Signals

  - Then connect Waveform Graph to wire above

**	Turn Page

- Timing & Transition Measurements must connect to Formula

  - Timing & Transition Measurements Frequency to Formula f

  - Then connect numeric indicator 1 to connection wire above

- Formula must connect to numeric indicator 2

  - Formula Results to numeric indicator 2

- Change labels:

  - Numeric 1 and Numeric 2

  - To Hz and RPMs

- Change:

  - Numeric Indicators to display only integers

    - Example: Not 1034.56 but like 1034

  - Waveform Graph X-axis

    - To 0.01 from 0.1 for easy read display

- Challenge (Modification):

  - Once circuit and LabVIEW are working properly get Professor to sign off

Professor Sign x___________________

  - Create a warning light

    - If the motor speeds above 6000 RPMs - turn on warning light

- Analysis:

  - Answer the following questions in written paragraph form and turn in next week:

    - What type of input is this task?  Explain.

    - What parameters of the motor used to calculate frequency?

    - What is the result of having the wrong arithmetic comparison circuit?

- Write-up:

  - Do not write a formal lab report.

  - Turn in snap shots with demonstration of the above requirements.

  - Explain and answer the above questions