Control Systems

W. Lopez, CSULB – ET 360

Activity X – Thermistor Lab

- Objective of Lab:

  - The following concepts will be introduced and applied with the goal of becoming familiar with the LabVIEW application and its interface:

    - New Dialog Box and Template VIs

    - Front Panel

    - Block Diagram

    - Front Panel and Block Diagram Tools

    - Running and Stopping a VI

    - Express VIs

    - LabVIEW Documentation resources

    - Property Dialog Boxes

    - Shortcuts

- Procedure:

Block Diagram Panel

- Place a While loop on the Block Diagram

  - Right Click

  - Express

    - Exec Control

      - While Loop – make sure all components are inside

- DAQ Task

  - Right Click on Block Diagram

    - Measurement I/O

      - NI-DAQmx

        - Acquire Signals

        - Analog input

        - Voltage – select ai1

        - Click Finish

        - Max [10]; Min [-10] Voltage

        - Timing Settings

          - Click drop down menu

          - Select 1 Sample (On Demand)

        - Click, at bottom, OK

**	Turn Page

- Place Formula

  - Right Click on Block Diagram

    - Express

      - Arith & Com…

      - X1 – change Label to Invert

      - Hit Enter

      - Insert at top – Invert*(-1)

      - Click OK

- Place Add

  - Right Click on Block Diagram

    - Express

      - Arith & Com…

        - Numeric

          - Add

          - Place between DAQ and Formula

          - Connect DAQ data to Add (in)

          - Connect Add (out) to Formula Invert

Front Panel

- Place Thermometer

  - Right click on Front Panel

  - Numeric

    - Thermometer – place on Front Panel

      - Note: Change properties and Scale to your liking

- Place Numeric Control

  - Right click on Front Panel

  - Numeric

    - Numeric Co… - Place on Front Panel

      - Note: Rename Offset

- Place Gauge

  - Right click on Front Panel

  - Numeric

    - Gauge - Place on Front Panel

      - Note: Rename Offset

**	Turn Page

- Place Numeric Indicator

  - Right click on Front Panel

  - Numeric

    - Numeric Indi… - Place on Front Panel

      - Note: Rename Gauge Numeric

Block Diagram Panel

- Connections

  - Increase size of While Loop and organize Vis

  - Connect or wire DAQ data to Gauge

  - Connect or wire DAQ data to Gauge Numeric

  - Connect Offset to Add (In)

  - Connect Formula Result to Thermometer

    - But move Thermometer to the right of Formula, first.

- Challenge (Modification):

  - Once circuit and LabVIEW are working properly get Professor to sign off

Professor Sign x___________________

  - Add an actual Thermometer to measure room and change in temperature.

    - Hint: You need a Formula which will convert circuit voltage to temp.

  - Uber Macho modification

    - Create a second circuit in LabVIEW, which will take a “snapshot” and place it in the offset numeric control.  This will replace the need for the operator to read the gauge and manually place it in the offset control.

- Analysis:

  - Answer the following questions in written paragraph form and turn in next week:

    - Why is it necessary to amplify the signal from the Thermistor?

    - Why must we invert the signal from the input in software?

    - What is the difference between 1k and 10k Sampling?

- Write-up:

  - Do not write a formal lab report.

  - Turn in snap shots with demonstration of the above requirements.

  - Explain and answer the above questions