| Control Systems W. Lopez, CSULB – ET 360 |  |
| --- | --- |

## Activity 3 – Analyzing and Saving a Signal				3

- Objectives of Lab 3:

  - The following concepts will be introduced and applied with the goal of Building and Analysis VI within LabVIEW:

- Modifying a VI created from a template

- Adding a signal

- Adding two signals (Mixing waveforms,  adding Noise)

- Filtering a signal

- Analyzing the amplitude of a signal: Measuring a Peak-to-Peak digitally

- Creating warning

  - lights, setting warning level limits, user warning

- Saving data to a file

- Procedure:

  - Work through Chapter 3 ( pages 3-1 through 3-17) in the Getting Started with LabVIEW document (either pdf file or printed manual).

  - Execute the activities in the LabVIEW program version available to you/your group.

  - Demonstrate to instructor and/or document when complete modifications (by page 3-12 and 3-16). Include an image or screen-shot of the Front Panel and Block Diagram at these points in your document to be turned in.

  - Save your new VI with a new filename.

- Synthesis:

  - Using your new VI:

    - Copy and paste waveform graph and block diagram  into your document to be turned in at the following points of completion:

      - After completing step 11 on page 3-8 and  after step 6 on page 3-12

    - Copy and paste the header and some sample data (showing the data when you pressed the ‘Write to File’ Boolean control into your document).

- Analysis:

  - Answer the following questions and turn in next week

    - What are the five different filter conditioning types available in the Filter Express VI?

    - The Waveform Graph VI is analogous to an Oscilloscope.  In this lab we added some Express VIs that now add the features of a Digital Storage Oscilloscope – What VIs used in this lab activity represent functions of a digital storage oscilloscope?.

    - What is the difference between the Switch and Latch Boolean <Control> Operation Conditions?

- Write-up:

Do not write a formal lab report. Turn in a document with the required screen shots and the answers to Analysis questions i – iii next week.