| Control Systems W. Lopez, CSULB – ET 360 |  |
| --- | --- |

## Activity 7 – Creating DAQ within LabVIEW	using DAQ Assistant Express VI		7

- Objectives of Lab 7:

  - The following concepts will be introduced and applied with the goal of creating DAQ tasks within LabVIEW:

- Use of the DAQ Assistant Express VI for DAQ configuration.

- Review of Task configuration.

- Instrument Drivers

- Instrument I/O Assistant Express VI.

- Understanding and Integrating external sensing (LM34) component

- Integrating external circuitry (LM34) to the USB-6008

- Procedure:

  - Refer to the LM34 datasheet for this activity for instrument parameters.

  - Wire your LM34 to the USB-6008 DAQ device as follows:

to Pin 31

to Pin 2

to Pin 32 & Pin 3

  - Work through the “Getting Started with LabVIEW” Chapter 4 (pages 4-1  through 4-6:  Stop at the “Communicating with an Instrument” section on page 4-6).

  - When completing the  “Editing the NI-DAQmx Task”, note that you do not need to physically add any second instrument to the USB6008.  Any voltage signal detected on this unused channel is noise – ignore it.

  - Execute the activities in the LabVIEW program version available to you/your group.

  - Demonstrate to instructor when complete modifications (by page 4-6). Include an image or screen-shot of the Front Panel and Block Diagram at this point  in your document to be turned in.

  - Save your new VI.

- Synthesis:

  - Using your new VI:

    - Copy and paste an image of the front panel and block diagram of  read voltage.vi  running with your USB-6008 providing input.

    - Add two different front panel numeric indicators to the VI.

- Analysis:

  - Read the  LM34 datasheet and then answer the following questions and turn in next week

    - What are the characteristics of the LM34 from the datasheet?

      - Include: Input voltage range, output voltage range,  output temperature range, scale factor, scale characteristics

    - Does the instrument you created using the LM34-USB6008-LabVIEW have the same response characteristics as stated for the LM34 component alone?

    - What is the intended environment that the LM34 is designed to ‘sense?’

- Write-up:

Do not write a formal lab report. Turn in a document with the required screen shots and the answers to Analysis questions i – iii next week.