Control Systems

W. Lopez, CSULB – ET 360

Activity W – Motor Speed Control

- Objective of Lab:

  - The following concepts will be introduced and applied with the goal of becoming familiar with the LabVIEW application and its interface:

    - New Dialog Box and Template VIs

    - Front Panel

    - Block Diagram

    - Front Panel and Block Diagram Tools

    - Running and Stopping a VI

    - Express VIs

    - LabVIEW Documentation resources

    - Property Dialog Boxes

    - Shortcuts

- Procedure:

Motor and DAQ Connections

- Attach DAQ to computer through USB cable

  - Motor leads:

    - Blue – (-)

    - Red – (+)

  - Connect the motor  drive circuit

- Tachometer (DO NOT CONNECT):

    - Yellow – (+)

    - Green – (-)

Block Diagram Panel

- Place a While loop on the Block Diagram

  - Right Click

  - Express

    - Exec Control

      - While Loop – make sure all components are inside

**	Turn Page

- Place Simulate Signal

  - Right Click

  - Express

    - Signal Analysis

      - Simulate Signal

        - Signals

          - Signal type – Square

          - Frequency (Hz) – 100.1

          - Amplitude – (+2.5 VDC)

          - Offset – (+2.5 VDC)

          - Duty cycle (%) – 50

        - Timing

          - Samples per second (Hz) – 1000

          - Number of samples:  1000

          - Run as fast as possible

        - Time Stamps

          - Relative to start of measurement

        - Reset Signal

          - Use continuous generation

Front Panel

- Place Waveform Graph

  - Right click

  - Express

    - Graph Indicat…

      - Graph - place next to STOP button

      - Go to Properties (Right Click on Waveform Graph)

        - Scales

          - Click Autoscale

            - Minimum – 0

            - Maximum – 0.035

          - Click drop down arrow Time (X-Axis)

            - Select Amplitude (Y-Axis)

            - Click Autoscale

            - Minimum – (-10)

            - Maximum – (10)

            - Close OK

**	Turn Page

- Place Pointer Slider

  - Right Click

  - Express

    - Num Ctrls

    - Pointer Slider - place left of Waveform Graph

      - Go to Properties

        - Scale

          - Scale Range

            - Minimum – 0

            - Maximum – 100

            - Click OK

Block Diagram Panel (2)

- Make room inside while loop as necessary

- DAQ Task Const

  - Right Click

    - Measurement I/O

      - NI-DAQmx

        - Task Const – Place above and to the right of Simulate Signal

        - Click Drop Down Menu – Browse

        - Create New… - MAX Task

        - Generate Signals

        - Analog Output

        - Voltage – select ao0

        - Click Next >

        - Give your task a name – Click Finish

        - Timing Settings

          - Click drop down menu

          - Select 1 Sample (On Demand)

        - Click, at bottom, OK

        - Click OK

- DAQ Task Const

  - Right Click

  - Measurement I/O

    - NI-DAQmx

      - Write – Place below and to the right of DAQmx Task Name

        - Wire should automatically connect (If not connect)

        - Wire from DAQmx Task Name to DAQmx Write task/channels in

- Then wire Simulate Signal Square to DAQmx Task Write Data

- Move Waveform Graph to right of Simulate Signal

- Wire Simulate Signal square to Waveform Graph in

- Wire Slide to Simulate Signal Duty Cycle (%)

- Change labels:

  - Slide to Pulse Width

**	Turn Page

- Challenge (Modification):

  - Once circuit and LabVIEW are working properly get Professor to sign off

Professor Sign x___________________

  - Improve the smoothness of the motor

    - Hint: How can you change the speed displayed on the Waveform Graph??

  - Uber Macho modification

    - Combine previous lab with this current lab

    - Measure speed of this motor lab in LabVIEW

- Analysis:

  - Answer the following questions in written paragraph form and turn in next week:

    - What type of task is this?  Explain.

    - What parameters of the waveform are used to change the speed?

    - What is the result of having the wrong speed displayed on the screen?

- Write-up:

  - Do not write a formal lab report.

  - Turn in snap shots with demonstration of the above requirements.

  - Explain and answer the above questions

# Text boxes

Gnd

Ao0

+12V

1k

TIP 102